## Slide 1
HAND GESTURE CONTROLLED WHEELCHAIR
Objective:
Driving a “traditional wheelchair” is an effortful task for the elderly & disabled.
Our project aims to provide a user-friendly experience of wheelchair driving using simple hand gestures.
Block diagram Transmitter section:
Arduino Uno
ADXL335
Accelerometer
433Mhz RF Transmitter
Power Supply
Hand Gestures
Block diagram Receiver section:
433MHz RF Receiver
Power Supply
Arduino Uno
DC Motors
L293D
DC Motor Driver
Encoded message from the transmitter
Ultrasonic Sensor
Obstacles/Hurdles
Buzzer

## Slide 2
HAND GESTURE CONTROLLED WHEELCHAIR
Gesture | X-range | Y-range
Forward | 325<x<340 | 265<x<290
Backward | 325<x<340 | 365<x<395
Right | 380<x<425 | 310<x<330
Left | 205<x<350 | 310<x<330
Stop | 320<x<350 | 320<y<350
RF Transmitter
MEMS Accelerometer
Arduino Uno
Result:
Range of Analog voltage output of the accelerometer:
Some features:
The use of RF modules enables seamless wireless communication.
The ADXL335 accelerometer is compact and light weight making it easy for the user to wear the device around his wrists.
Enables the user to be independent and safe.
RF Receiver
Ultrasonic sensor
Arduino Uno
Motor driver IC